## Slide 1: A Simple Task Scheduler for Microcontrollers
In C++
© 2024 Len Popp
Notes: © 2024 Len Popp. This work is licensed under a Creative Commons Attribution 4.0 International License.
https://creativecommons.org/licenses/by/4.0/
Time: approx. 20-25 mins

## Slide 2: Len Popp
Retired Software Guy, Software & Hardware Hobbyist
https://lenp.net/
Notes: I worked at ImageWare Systems for a long time
This is based on my hobby projects – I don’t have professional experience in embedded systems programming

## Slide 3: Agenda
What It Is
How to Use It
How It Works
Questions?
Notes: Feel free to ask questions

## Slide 4: Warning / promise
Contains “modern” C++
[&](){}();
Notes: Warning / promise: Not sure which it is
Will be showing some modern C++
Looks strange to someone like me

## Slide 5: What It Is

## Slide 6: Background
Embedded microcontroller
Firmware written in C++
Firmware must perform multiple tasks
No operating system (RTOS)
  Small-to-medium microcontroller
  Programming with an SDK over the bare metal
Want a simple task scheduler to help with simple projects
Notes: Embedded microcontroller in a device
...
Want a simple task scheduler
  In lieu of a proper OS, this is the kernel of a kernel

## Slide 7: Example: Dexy
Digital FM synth module
Based on a Raspberry Pi Pico(-ish)
Firmware runs a task scheduler for low-priority tasks, including:
  UI (display and rotary encoder)
  USB serial I/O
  Other tasks for testing, debugging, etc.
Task scheduler is not used for audio synthesis
  Interrupt-driven for timing precision
https://lenp.net/synth/dexy/
Notes: Module from a modular synthesizer, which I made, that does digital audio synthesis

## Slide 8: Demo
Adafruit Feather RP2040
  Raspberry Pi Pico-compatible board
Two tasks:
  Blinking LED
  Colour-cycling RGB LED
https://github.com/Len42/TaskDemo-RP2040

## Slide 9: Simple Task Scheduling
Several independent tasks to run “simultaneously”
Round-robin execution
Each task specifies how often it wants to run
When called, each task performs an increment of work
Very little overhead
  Microcontroller’s performance and memory are limited

## Slide 10: What It Doesn’t Do
Not suitable for tasks with hard real-time requirements
No task pre-emption
No long-executing functions allowed
  Tasks must be broken up into bite-size increments
  For example, must use non-blocking calls for internet requests.
Tasks not guaranteed to run precisely on time

## Slide 11: Hardware Requirements
Not much!
Clock/timer for elapsed time
  Millisecond or microsecond resolution
Interrupts not required
Notes: Clock/timer for elapsed time: Any microcontroller has this

## Slide 12: Software Requirements
C++ 20
  Can be implemented in “traditional” C++ with a bit more boilerplate code
Elapsed time function
  From device SDK

## Slide 13: How To Use It
Writing firmware with tasks

## Slide 14: Main()
Tasks::TaskList defines the list of Task classes to be executed
  Commented-out tasks are not compiled
initAll calls each Task’s init function
runAll calls each Task’s execute function
  Called in order listed
Loop forever
// Task List
constexpr Tasks::TaskList<
//DebugTask,
LedBlinkTask,
LedColourTask
> taskList;
int main()
{
// Initialize all the Tasks and run them forever
taskList.initAll();
while (true) {
taskList.runAll();
}
}
Notes: This is the main() code running on the demo board.
  taskList is initialized at compile time
  Hence the funny brackets <>
Lots of constexpr & consteval used to force things to be done at compile time

## Slide 15: Example Task
Task to blink an LED
Class encapsulates everything, so this task is independent of other code
Class is a subclass of Tasks::Task
Implements 3 virtual functions
Not necessary to declare an instance of LedBlinkTask
  Done automatically by Tasks::TaskList
// LedBlinkTask: Task to blink an LED on & off
class LedBlinkTask : public Tasks::Task
{
public:
// Task execution interval in microseconds
unsigned intervalMicros() const override { return 500'000; }
// Task initialization, called once at program start
void init() override {
gpio_init(PICO_DEFAULT_LED_PIN);
gpio_set_dir(PICO_DEFAULT_LED_PIN, GPIO_OUT);
gpio_put(PICO_DEFAULT_LED_PIN, false);
}
// Main task function
void execute() override {
fLed = !fLed;
gpio_put(PICO_DEFAULT_LED_PIN, fLed);
}
private:
bool fLed = false;
};
Notes: This is one of the tasks running on the demo board
Implements 3 virtual functions:
  intervalMicros() specifies how often the task should run
  init() is called once at startup
  execute() is called as required – must be a short snippet of work
Not necessary to declare an instance of the Task
  This was one of the drivers for me to create the crazy template code to be shown later
  I don’t like having to define/declare things in 2 places – annoying and error prone

## Slide 16: How It Works
It’s not rocket science
It’s C++ magic

## Slide 17: Task Base Class
Abstract base class
  Pure virtual functions implemented by task subclasses
tick is called frequently by the task scheduler
  If it’s time to execute this task, call execute
timer keeps track of the next time to run the task
taskInstance is a variable template that creates a single instance of each Task subclass
class Task
{
public:
virtual unsigned intervalMicros() const = 0;
virtual void init() = 0;
virtual void execute() = 0;
void tick(absolute_time_t now)
{
if (timeIsReached(now, timer)) {
timer = make_timeout_time_us(intervalMicros());
execute();
}
}
private:
absolute_time_t timer = from_us_since_boot_constexpr(0);
};
template<typename TASK_T>
static TASK_T taskInstance;
Notes: tick() is implemented with Pi Pico SDK functions & types
Can work on any other microcontroller, coded appropriately

## Slide 18: Task Scheduler
This is the type of taskList seen earlier
Template arguments are the Task subclasses
Contains an array of Task*
Constructor initializes the list of tasks
  consteval – executes at compile time
C++ magic turns a list of class names into a list of Task instances
Iteration by fold expression over parameter pack
template<typename... TASKS>
class TaskList
{
public:
consteval TaskList()
{
int i = 0;
((tasks[i++] = &taskInstance<TASKS>), ...);
}
void initAll() const /* ... */
void runAll() const /* ... */
private:
Task* tasks[sizeof...(TASKS)];
};
// in main.cpp (as seen before):
constexpr Tasks::TaskList<
//DebugTask,
LedBlinkTask,
LedColourTask
> taskList;
Notes: Declaration from main.cpp included at the bottom
Variadic template – parameter pack
“sizeof…(TASKS)” gives the number of template arguments
(C++20 warning): Constructor is declared consteval – necessary for compile-time initialization
taskInstance<> is the variable template defined earlier
  Refers to one instance of the given class

## Slide 19: Task Scheduler (cont.)
Implements the initAll and runAll functions
template<typename... TASKS>
class TaskList
{
public:
consteval TaskList() /* ... */
void initAll() const
{
for (auto&& task : tasks) {
task->init();
}
};
void runAll() const
{
absolute_time_t now = get_absolute_time();
for (auto&& task : tasks) {
task->tick(now);
}
};
private:
Task* tasks[sizeof...(TASKS)];
};
Notes: Device-specific code

## Slide 20: Outro

## Slide 21: What I Like
Tasks are modular, independent
  Good code organization
  Easy to add and remove tasks (debugging etc.)
Each task has its own repetition interval
Low overhead
  No heap memory allocation
  A few bytes per task compared to inline code

## Slide 22: What I don’t Like
Not suitable for tasks with hard real-time constraints
  A long-running task blocks other tasks from running

## Slide 23: download
https://github.com/Len42/TaskDemo-RP2040
Notes: Or go to lenp.net

## Slide 24: FIN
Questions?
Notes: Thank you.